## Slide 1: What’s the Impact?
Lessons
Mid-American and Alliant service
Net metering
Home Construction Matters
  Roof line
  HVAC system
  Tightness
Solar panels save our families a lot of money
Clarifications and Framework
Tracked by month of usage, not date of bill
Average daily usage (except one home)
  Monthly billing cycle has varying number of days
Estimates on costs due to budget billing
Track electric charges but not electric bill
  Each utility has varying service and connection fees

## Slide 2: Impact- 253 Sierra Park Drive
House Facts | 
Roof Slope | South
Heating | Gas
Insulation | Spray foam, exterior hardboard
Year Constructed | 2019
Array Size | 4.25 kW
Chart: Total Electric Usage (KwH)
| September | October | November | December | January | February | March | April
Usage Pre Panels | 1174 | 977 | 941 | 853 | 821 | 696 | 773 | 977
Usage Post Panels | 552 | 227 | 450 | 719 | 223 | 281 | 310 | 729
Chart: Electric Charges
| September | October | November | December | January | February | March | April
Pre Panels | 193.09 | 154.2 | 153.83 | 143.41 | 138.36 | 110.73 | 135.21 | 156.74
Post Panels | 99.22 | 50.94 | 78.83 | 117.52 | 47.86 | 58.74 | 61.1 | 64.17
Chart: Savings on Electric Charges
| September | October | November | December | January | February | March | April | May
 | 93.87 | 103.26 | 75 | 25.89 | 90.5 | 51.99 | 74.11 | 92.57

## Slide 3: Impact- 223 Sierra Park Drive
House Facts | 
Roof Slope | South
Heating | Gas
Insulation | Spray foam, exterior hardboard
Year Constructed | 2017
Array Size | 5.1 kW
Chart: Average Daily Net Usage (KwH)
| Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May
Usage Pre Panels | 18.6552 | 16.8621 | 18.0938 | 20.0645 | 18.25 | 17.3929 | 15.8966 | 16.7 | 17.8788
Usage Post Panels | -3.3125 | -0.5 | 6.5667 | 11.1818 | 1.069 | 1.25 | -6 | -4.9655 | -4.9655
Chart: Electric Charges
| Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May
Pre Panels | 83.5493 | 76.11 | 90.12 | 97.12 | 90.89 | 76.11 | 61.4006 | 71.9257 | 91.0606
Post Panels | -12.7635 | -2.64 | 30.77 | 58.68 | 4.99 | 5.95 | -13.07 | -30.12 | -24.16
Chart: Savings on Electric Charges
| Sep | Oct | Nov | Dec | Jan | Feb | Mar | Apr | May
$96.31 $78.75 $59.35 $38.44 $85.90 $70.16 $74.47 $102.05 $115.22 | 96.3128 | 78.75 | 59.35 | 38.44 | 85.9 | 70.16 | 74.4706 | 102.0457 | 115.2206

## Slide 4: Impact-605 8th Ave
House Facts | 
Roof Slope | South
Heating | Gas
Insulation | Spray foam, exterior hardboard
Year Constructed | 2016
Array Size | 4.25 kW
Chart: Average Daily Net Usage (KwH)
| October | November | December | January | February | March | April | May
Usage Pre Panels | 23.1379 | 21.4138 | 15.6333 | 14.4848 | 18.0345 | 15.3103 | 13.55 | 16.8438
Usage Post Panels | 15.5517 | 12.2581 | 15.3143 | 12.7742 | 11.2812 | 13.8 | 15.1071 | 16.0345
Chart: Electric Charges
| October | November | December | January | February | March | April | May
Pre Panels | 53.98 | 49.95 | 37.73 | 38.45 | 42.07 | 35.7154 | 31.6129 | 43.3572
Post Panels | 20.22 | 16.79 | 48.16 | 20.34 | 6.38 | 14.63 | 13.96 | 16.07
Chart: Savings on Electric Charges
| October | November | December | January | February | March | April | May
Savings | 33.76 | 33.16 | -10.43 | 18.11 | 35.69 | 21.0854 | 17.6529 | 27.2872

## Slide 5: Impact-2653 Blazing Star
House Facts | 
Roof Slope | East, West
Heating | Heat Pump
Insulation | Spray foam, exterior hardboard
Year Constructed | 2021
Array Size | 4.74 kW
Chart: Electric Charges
| October | November | December | January | February | March | April
Pre Panels | 61.13 | 92.1 | 127.58 | 114.71 | 118.65 | 90.33 | 61.9388
Post Panels | 43.11 | 81.3 | 121 | 128.35 | 87.34 | 32.32 | 17.02
Chart: Average Daily Net Usage (KwH)
| October | November | December | January | February | March | April
Usage Pre Panels | 24.52 | 36.94 | 46.65 | 47.53 | 47.58 | 36.23 | 26.5517
Usage Post Panels | 16.1 | 31.29 | 45 | 51.34 | 32.43 | 11.9655 | 5.6875
Chart: Savings on Electric Charges
| October | November | December | January | February | March | April
Savings | 18.02 | 10.8 | 6.58 | -13.64 | 31.31 | 58.01 | 44.9188